## Slide 1
Racing on Scenic
A Domain Built On Top of Driving
By: Lawrence Shieh
Open
1 / 46

## Slide 2
Racing on Scenic: A Domain Built On Top of Driving
• Lawrence Shieh (5th Year MS Student)
• Presentation Focus: Scenic's class / region / behavior model carried us through ~67 mph racing -- with two specific gaps we'll itemize at the end
• 3-topic roadmap: scenarios -> racing library -> dSPACE bridge -> feedback
• Code-tour interleaved -- code anchors are clickable; open the repo now
VIDEO PLACEHOLDER
8s loop of IAC car on F-bank as visual hook
> src/scenic/domains/racing/ (root)
Open
2 / 46

## Slide 3
Why Racing Stresses Scenic Differently
• Closing speeds ~67 mph (30 m/s) vs. urban driving's ~22 mph (10 m/s)
• Oval / road-course geometry, not grid lanes
• Competitive intent (overtake, block) needs strategy, not just maneuvers
• Falsification has hard real-time cost (dSPACE wall-clock)
> src/scenic/domains/racing/model.scenic:125-196 (RacingCar delta)
Open
3 / 46

## Slide 4
Roadmap & Today's Deliverable
• Topic 1: scenario banks -- F-bank (regression) + falsifiable (exploration)
• Topic 2: racing library internals -- geometry, behaviors, MPC, planner, falsifier
• Topic 3: dSPACE bridge -- light architectural sketch
• Closing: two concrete asks with API sketches and implementation paths
• Time: ~30 min slides + ~25 min live code + ~5 min Q&A
Open
4 / 46

## Slide 5
Topic 1
Scenarios -- two banks, one shared library
Topic 1: Scenarios
5 / 46

## Slide 6
Two Scenario Banks, One Shared Library
• F-bank -- regression suite, 13 scenarios (F0-F12), hardcoded positions
• Falsifiable -- one .scenic file (S1_falsify), distribution-driven
• Same .scenic file shape across both; only the parameter type differs
• F-bank locks specific failure modes; falsifiable explores parameter space
> examples/racing/ (browse f_shared/ and falsifiable/)
Topic 1: Scenarios
6 / 46

## Slide 7
F-Bank Walk: F0-F5 (Solo and Reactive Fellows)
• F0 ego-only baseline (no fellow)
• F1 fellow behind, no interaction
• F2 ahead, slower -- the overtake setup
• F3L / F3R side-blocked (left or right TTL)
• F4 sudden stop -- SuddenStopInterval behavior
• F5 swerve -- SwerveOutOfControl behavior
VIDEO PLACEHOLDER
dSPACE viewer F4 emergency-brake event, ~20 s
> examples/racing/f_shared/F4_fellow_ahead_sudden_stop.scenic
Topic 1: Scenarios
7 / 46

## Slide 8
F-Bank Walk: F6-F12 (Geometric and Strategic)
• F6 / F7 strict left / right occupied (passing-side forced)
• F8 corner + ahead -- by-design conservatism
• F9 stationary roadside obstacle (speed=0 given to fellow behavior)
• F10 / F11 / F12 corner-entry variants (left/right/stop)
• Each scenario regresses against a specific failure mode
VIDEO PLACEHOLDER
F9 stationary obstacle clip showing ego cruising past with speed=0 fellow, ~20 s
> examples/racing/f_shared/F9_fellow_stationary_roadside_obstacle.scenic
Topic 1: Scenarios
8 / 46

## Slide 9
Falsifiable Bank: S1_falsify.scenic
• One file: examples/racing/falsifiable/S1_falsify.scenic (~50 LOC)
• Key line: gap_m = VerifaiRange(20, 60) -- the only special syntax
• Everything else is plain Scenic (model, ego, opponent, behaviors)
• Sampler chosen at runner-time: --sampler {halton, ce, bo, random}
• Halton -> uniform coverage; CE -> active falsification (we'll see CE results in Topic 2c)
> examples/racing/falsifiable/S1_falsify.scenic:41
Topic 1: Scenarios
9 / 46

## Slide 10
Topic 2a
Geometry -- RacingCar, RacingTrack, regions, TTL
Topic 2a: Geometry
10 / 46

## Slide 11
Inheritance Chain: Vehicle -> Car -> RacingCar
• Vehicle driving/model.scenic:268
• Car driving/model.scenic:298
• RacingCar racing/model.scenic:125
• RacingCar adds: raceNumber, IAC dims (1.93 x 4.88 m / 76 x 192 in), maxSpeed=~67 mph, ttlFolder, ttlFileName
• Total delta: ~70 lines
> src/scenic/domains/racing/model.scenic:125-196
Topic 2a: Geometry
11 / 46

## Slide 12
What RacingCar Adds: Field-by-Field Explanation
• Identity: raceNumber, team, carType -- needed by dSPACE traffic + eval logs
• Geometry: width=1.93 m, length=4.88 m -- IAC Dallara AV-24; drives the OBB collision check
• Performance envelope: maxSpeed=~67 mph, accel=8 m/s^2, braking=-12 m/s^2 -- feeds planner + MPC speed cap
• State (aspirational): fuelLevel, tireWear -- extension points for endurance scenarios; not used today
• Controller knobs: waypointTolerance=2.5 m, controllerAggressiveness=0.5 -- MPC tuning
• TTL routing: ttlFolder, ttlFileName -- per-vehicle racing-line selection
> src/scenic/domains/racing/model.scenic:125-196
Topic 2a: Geometry
12 / 46

## Slide 13
The Default Position Trick
• position: new Point on ttlRegion(self.ttlFileName)
• Self-referential default: depends on this car's ttlFileName property
• Composes with inherited parentOrientation = (roadDirection at position) + roadDeviation
• Result: `new RacingCar` with no specifiers = track-aligned car at a valid TTL position
• Explicit specifiers (`new RacingCar on mainTrack`) still override
> src/scenic/domains/racing/model.scenic:164
Topic 2a: Geometry
13 / 46

## Slide 14
RacingTrack: Wrapping Scenic's Network
• Scenic's driving domain provides Network -- parsed from XODR (OpenDRIVE)
• Network gives us roads, lanes, intersections, centerlines, lane edges
• RacingTrack (segments/tracks.py) is a Python class that wraps that Network
• It identifies main-loop roads vs. pit-lane roads via topology + name patterns
• Exposes: track.network, track._mainRacingRoads, track._pitRoads
> src/scenic/domains/racing/segments/tracks.py:807-852
Topic 2a: Geometry
14 / 46

## Slide 15
Region Composition: mainTrack, pitTrack, ttlRegion
• mainTrack, pitTrack -- buffered polygons around road centerlines (XODR-native)
• ttlRegion(file) -- buffered polygon around a TTL CSV centerline (per-line)
• Ego placement: explicit `on mainTrack` OR per-vehicle default `on ttlRegion(self.ttlFileName)`
• TTL CSV format: x, y, z columns (3D centerline waypoints)
• Multiple TTLs per track: optimal, left, right, pit
> src/scenic/domains/racing/segments/track_regions.py:275-352
Missing from Scenic: no first-class Frenet/RD region.
Topic 2a: Geometry
15 / 46

## Slide 16
The Frenet Gap (Foreshadow)
• Every racing scenario reasons in (s, t) coordinates
• Scenic gives us (x, y) regions; conversion is per-simulator
• We built a parallel RD frame in Python (~30 LOC, dSPACE-only)
• Surface today: dSPACE specifier `_racing_st_offset` (Topic 3)
• Proposal at close: Scenic core could absorb this
> src/scenic/simulators/dspace/modeldesk/placement.py:26-58
Topic 2a: Geometry
16 / 46

## Slide 17
Topic 2b
Behaviors + MPC -- the star behavior, planner, FSM, safety
Topic 2b: Behaviors + MPC
17 / 46

## Slide 18
The Star Behavior: FollowRacingLineMPCBehavior
• Defined at behaviors.scenic:310 (signature with ~13 kwargs)
• Main loop spans lines 554-2840 (yes, ~2300 lines)
• Called from every ego scenario in F-bank and falsifiable
• Composes with `try-interrupt` for events (collisions, mode switches)
> src/scenic/domains/racing/behaviors.scenic:310
Topic 2b: Behaviors + MPC
18 / 46

## Slide 19
The 8-Phase Tick (Survey)
• 1. State read (sim/dSPACE readback)
• 2. Waypoint progress (advance index on current TTL -> gives ego arc-length `s`)
• 3. Tactical planner (uses `s`; picks TTL + speed cap)
• 4. MPC reference build (sample chosen-TTL waypoints over horizon)
• 5. Lateral MPC -> steering
• 6. Longitudinal MPC -> throttle / brake
• 7. Gear logic (rule-based, post-MPC)
• 8. Safety gates -> action emit
> src/scenic/domains/racing/behaviors.scenic:554-2840
Topic 2b: Behaviors + MPC
19 / 46

## Slide 20
Lateral MPC (Deep Into Params)
• State: [e_y, e_psi, delta, s] (cross-track err, heading err, steer, progress)
• Control: steering rate (rad/s) -- integrated to delta
• Solver: OSQP (sparse QP); ~5-10 ms per tick
• Horizon: 35 steps x 0.05 s = 1.75 s (the LOCAL tracking horizon)
• Reference: TTL spline -> (x_ref, y_ref, psi_ref, kappa_ref) per horizon step
• Cost: contouring (e_y, e_psi) + smoothness (delta_rate^2) + progress reward
> src/scenic/domains/racing/mpc/reference_builder.py:14-200
Topic 2b: Behaviors + MPC
20 / 46

## Slide 21
Longitudinal MPC + Gear Logic (Deep Into Params)
• State: [v, a] -- velocity, acceleration
• Control: [throttle, brake] in [0, 1]^2
• Same 1.75 s horizon as lateral
• v_target from TTL line (curvature-aware speed cap: v_max = sqrt(a_y_max / kappa))
• Coupling: longitudinal v feeds lateral kappa lookup
• Gear logic: rule-based AFTER MPC (proactive downshift before high-curvature)
> src/scenic/domains/racing/behaviors.scenic:554-2840
Topic 2b: Behaviors + MPC
21 / 46

## Slide 22
Tactical Planner: The Strategic Layer
• Picks one of 4 strategies: stay_optimal, follow_fellow, pass_left, pass_right
• Trajectory prediction: fellow over 10 s horizon (constant-velocity model)
• Strategy simulator: rolls out each candidate; ranks by progress + min-clearance
• Output: planner mode + chosen TTL + speed cap
• Then hands the chosen mode to the executor state machine (next slide)
> src/scenic/domains/racing/tactical_planner.py:350-430
Topic 2b: Behaviors + MPC
22 / 46

## Slide 23
The Executor State Machine -- Hand-Rolled FSM
• 5 logical states (COMMIT/HOLD have L/R variants -> 7 constants)
• Initial: FREE_RUN; no terminal state
• Storage: `TacticalPlannerState.mode: str = FREE_RUN`
• Transitions: chained `if state.mode == X` branches
• Entry actions: inlined Python beside each `state.mode = X`
• Output: (mode, ttl, speed_cap, decision_reason) per tick
Planner state machine
FREE_RUN
FOLLOW
COMMIT_PASS L/R
ABORT_PASS
HOLD_PASS L/R
fellow ahead
clear
strategy=pass
collision risk
lateral clear
merge safe
recovered
> src/scenic/domains/racing/tactical_planner.py:330-396
Missing from Scenic: no native state-machine construct for behaviors.
Topic 2b: Behaviors + MPC
23 / 46

## Slide 24
Safety Gate: Predicted-Collision Override
• path_collision_predicted(ego_path, opp_trajectory, horizon_s=1.5)
• Sample dt 0.1 s -> 15 samples per check
• Min clearance threshold: 0.5 m (hard overlap)
• Debounced (2 consecutive breaches) to handle numerical noise
• Independent of strategy layer -- can override even mid-COMMIT
> src/scenic/domains/racing/assessment/pass_geometry.py:194-240
Topic 2b: Behaviors + MPC
24 / 46

## Slide 25
Fellow Behaviors (Brief)
• FellowFollowTTLGeometricBehavior -- thin Scenic wrapper at behaviors.scenic:183-207
• Real logic: compute_follow_ttl_geometric_plant_command in fellow/commands.py:688-700
• Per tick: constant v_kmh + delta(s) feedforward from TTL waypoint table; no PID, no MPC
• FellowSuddenStopIntervalBehavior -- periodic stops (F4); FellowSwerveOutOfControl (F5)
• Adversarial in EFFECT (causes trouble for ego) but not LEARNING -- scripted disturbances
> src/scenic/domains/racing/fellow/commands.py:688-700
Topic 2b: Behaviors + MPC
25 / 46

## Slide 26
Topic 2c
Falsification -- the runner, monitors, and the 50-sample result
Topic 2c: Falsification
26 / 46

## Slide 27
The Falsifier Loop -- One Runner, Pluggable Sampler
• verifai_runner.py -- single in-process runner; handles every sampling mode
• Compiles scenario once; cosim bridge stays warm across ALL samples
• ~30 s VEOS init paid once per campaign, regardless of sample count
• Sampler swap via --sampler {halton, ce, bo, random}; same .scenic, same logs
• Halton = quasi-random coverage smoke; CE = active falsification
> src/scenic/domains/racing/benchmarks/verifai_runner.py
Topic 2c: Falsification
27 / 46

## Slide 28
Inside the Loop -- main() Walkthrough
• Setup (once per campaign):
• scenarioFromFile(file, params={'verifaiSamplerType': args.sampler}) -- compile, inject sampler
• simulator = scenario.getSimulator() -- spawns cosim bridge on first .simulate()
• Per sample (count iterations):
• scene = scenario.generate(feedback=last_rho) -- VerifAI's CE picks next gap
• simulator.simulate(scene) -- stdout teed to logs/sample_NNN.log
• metrics = parse_sample(log_path) -- regex-extracts SampleMetrics from STDOUT
• rho = monitors.RESOLVE[args.monitor](metrics) ; feedback = rho
• Caveat: monitors read PARSED STDOUT, not in-memory state -- a logging change would silently break this
> src/scenic/domains/racing/benchmarks/verifai_runner.py:352
Topic 2c: Falsification
28 / 46

## Slide 29
Monitors -- Robustness Predicates Over a Run
• collision -- bbox_gap_m_min: minimum bounding-box gap (meters); 0 = touch, <0 = overlap
• track -- track_clearance_m: signed distance to nearest track edge (meters)
• off-track / brake / overtake-success -- semi-continuous count signals
• safety = min(collision, track) -- two-spec composite (the one we used in the campaign)
• min -- four-way composite over all safety + planner signals
• all -- multi-objective tuple for `mab` (multi-armed bandit) samplers
> src/scenic/domains/racing/benchmarks/monitors.py
Topic 2c: Falsification
29 / 46

## Slide 30
The CE Run That Broke the Planner
• 50-sample cross-entropy run (--monitor safety, --time 3000)
• 29 / 50 collisions (58%)
• Collisions span gap in [21.7, 52.3] m -- broad failure, NOT a narrow cluster
• 6 successful overtakes (all via commit_pass_right)
VIDEO PLACEHOLDER
30 s replay of a representative collision (e.g. sample 11 gap=22.0m, or sample 17 gap=30.6m for a long-commit case)
> src/scenic/domains/racing/benchmarks/results/verifai_20260428_052048/
Topic 2c: Falsification
30 / 46

## Slide 31
What's Failing: Hypothesis from 50 Samples
• Striking asymmetry: 28 / 29 collisions involve LEFT-pass attempts only (1 mixed, 0 right-only)
• Pattern in left-pass collisions: 50-500 ticks of commit_pass_left_hold + 60-120 aborts -> contact
• Meanwhile: all 6 successful overtakes happened on COMMIT_PASS_RIGHT
• Open: TTL geometry on the left line? MPC lateral limits? Strategy preferring left over right?
• Off-track instrumentation invalid this run: ~10 m frame residual + 'd_in=0 = OUT' semantics
> src/scenic/domains/racing/tactical_planner.py:350-430
Topic 2c: Falsification
31 / 46

## Slide 32
The Pipeline Is the Deliverable
• 58% collision rate is a Smart-Ego result, NOT a pipeline-quality result
• Falsifier is ego-agnostic: ego is just a Scenic behavior assigned in the .scenic file
• Swap `FollowRacingLineMPCBehavior` for the ART stack -> falsify ART under the same scenarios
• Same .scenic, same monitors, same VerifAI sampler -- only `ego.behavior` changes
• The 28/29 left-only finding is ABOUT Smart Ego; another stack will surface its own asymmetries
> examples/racing/falsifiable/S1_falsify.scenic:55
Topic 2c: Falsification
32 / 46

## Slide 33
Topic 3
dSPACE -- VEOS, the cosim bridge, MAPort, _racing_st_offset
Topic 3: dSPACE
33 / 46

## Slide 34
Why dSPACE? VEOS in One Slide
• VEOS = dSPACE's HIL-compatible offline simulator
• Same Simulink model that ships to the real car (HIL parity)
• Co-simulation over IPC (deterministic stepping)
• Why it matters more than CARLA for our use case
> src/scenic/simulators/dspace/simulator.py:82-147
Topic 3: dSPACE
34 / 46

## Slide 35
dSPACE / Simulink / Real Racecar -- The Toolchain
• Simulink (MathWorks): graphical block-based vehicle dynamics model
• dSPACE: tooling stack on top of Simulink for automotive testing
• ModelDesk -- configures the model (roads, traffic, scenario params)
• ControlDesk -- runs experiments, displays variables
• VEOS -- pure-software simulator running the SAME Simulink model
• Real racecar: ECU runs compiled code generated from the same model
> src/scenic/simulators/dspace/simulator.py:82-147
Topic 3: dSPACE
35 / 46

## Slide 36
DSpaceSimulator + SyncStepBridge -- The Cosim Layer
• DSpaceSimulator.__init__ -- simulator.py:82-147
• createSimulation() -- simulator.py:237
• SyncStepBridge -- python_listener/sync_step_bridge.py:9-168
• IPC client (VeosCoSimTestClientIpc.exe) spawned at simulator.py:196-202
• Flow: Scenic process -> SyncStepBridge -> IPC client -> VEOS
> src/scenic/simulators/dspace/simulator.py:237
Topic 3: dSPACE
36 / 46

## Slide 37
MAPort: How State Crosses the Bridge
• MAPort = dSPACE's variable-access API (read/write Simulink signals)
• One MAPort variable per car / sensor / actuator
• Mapping is configuration-driven (no codegen)
• Latency dominated by VEOS step time, NOT bridge overhead
> src/scenic/simulators/dspace/simulator.py:544-686
Topic 3: dSPACE
37 / 46

## Slide 38
The `_racing_st_offset` Specifier
• Parser: placement.py:26-58 (parse `(s_offset, t_offset)` from a tuple)
• Resolution: placement.py:409-428 (reads ego's s,t at sim init, applies offset)
• Gives `(s, t)` placement against ego's TTL frame
• Lives outside Scenic core because Scenic has no Frenet primitive
• Works, but is dSPACE-only -- not portable to other simulators
> src/scenic/simulators/dspace/modeldesk/placement.py:409-428
Missing from Scenic: Frenet specifier should be domain-agnostic.
Topic 3: dSPACE
38 / 46

## Slide 39
Feedback
Two concrete asks for Scenic core
Feedback
39 / 46

## Slide 40
Constructive Feedback Frame
• Scenic's class / region / behavior model held up under racing pressure
• Two specific gaps surfaced: Frenet frames, state-machine behaviors
• Both are concrete proposals with API sketches and an implementation path
• Both come from real workarounds we wrote -- not speculation
• Neither is Scenic-was-wrong. Both are Scenic-could-grow.
Feedback
40 / 46

## Slide 41
Ask 1: First-Class Frenet Frame
• Workaround today: `_racing_st_offset` in placement.py:26-58 (~30 LOC, dSPACE-only)
• Confirmed not in Scenic core: zero matches for 'Frenet' / 's_offset' / 't_offset'
• Existing partial: LinearElement.flowFrom(point, distance) at roads.py:344 -- s only, no t
• Claim: Scenic core should expose `FrenetRegion(curve, s_range, t_range)` + `frenetOffset (s, t) from <obj>` specifier
• API sketch: `region = FrenetRegion(track.optimal_line, s=(0,100), t=(-3,3))` and `opp = new RacingCar with frenetOffset (gap_m, 5) from ego`
• Implementation: extend Polyline with frenet_at(s, t) (~30 LOC of projection math); specifier desugars to (x, y) at sample time
• Generalizes: any path-following domain (racing, ADAS lane-change, pedestrian crosswalks)
> src/scenic/simulators/dspace/modeldesk/placement.py:26-58
Feedback
41 / 46

## Slide 42
Ask 1: Same Logic, Side-by-Side
Today -- dSPACE-only specifier
# in S1_falsify.scenic:
opp = new RacingCar with \
_racing_st_offset (gap_m, 5)
# placement.py:26-58 (dSPACE-specific)
def _racing_st_offset_to_deltas(spec):
a, b = spec
if a == 'ahead': return (float(b), 0.0)
if a == 'left': return (0.0, float(b))
# ... 'behind', 'right', numeric tuple
# placement.py:409-428 resolution:
# reads ego._route_s_t at sim start,
# adds delta_s, delta_t,
# projects back to (x, y) via ego's
# route polyline.
# Lives outside Scenic core; ~30 LOC;
# dSPACE-only -- not portable.
Proposed -- Scenic core primitive
# in any .scenic file:
region = FrenetRegion(
track.optimal_line,
s=(0, 100), t=(-3, 3))
opp = new RacingCar with \
frenetOffset (gap_m, 5) from ego
# scenic/core/regions.py
class FrenetRegion(Region):
def __init__(curve, s_range, t_range):
...
def frenet_at(s, t):
x, y, h = curve.point_at(s)
return Vector(x - t*sin(h),
y + t*cos(h))
# Specifier desugars at sample time -> (x, y).
# Portable across all simulators.
> src/scenic/simulators/dspace/modeldesk/placement.py:26-58
Feedback
42 / 46

## Slide 43
Ask 2: First-Class State-Machine Behaviors
• Workaround today: state stored as `mode: str` on TacticalPlannerState dataclass (tactical_planner.py:330)
• Transitions: chained if/elif on `state.mode` inside `tactical_planner_step_v1()`; entry actions inlined ad-hoc beside every `state.mode = X` assignment
• Confirmed not in Scenic core: no `state` keyword in src/scenic/syntax/
• Existing primitive: `try-interrupt` (compiler.py:654-686) -- async transitions, but state must be hand-managed
• Claim: expose `state X:` blocks inside `behavior` definitions, with `on entry`, `on exit`, `when (cond): goto Y`
• Implementation: parser desugars `state` blocks into nested `try-interrupt` chains with a state variable; backwards-compatible (omit `state` = legacy behavior)
• Generalizes: every ADAS / autonomous-driving paper rolls its own FSM (CARLA examples, LGSVL navigators, our planner)
> src/scenic/domains/racing/tactical_planner.py:330-396
Feedback
43 / 46

## Slide 44
Ask 2: Same Logic, Side-by-Side
Today -- tactical_planner.py
if pick_left:
state.mode = COMMIT_PASS_LEFT
state.commit.side = 'left'
state.commit.start_s = sim_time_s
state.commit.until_s = sim_time_s + commit_hold_s
state.commit.candidate_count = ce_cycles
state.lateral_path_lock_side = 'left'
# ... 5 more entry-action lines
elif pick_right:
state.mode = COMMIT_PASS_RIGHT
# ... mirror image
elif state.mode == COMMIT_PASS_LEFT and lateral_clear:
state.mode = HOLD_PASS_LEFT
state.commit.hold_entry_s = sim_time_s
# ... mirror for COMMIT_PASS_RIGHT
elif state.mode == HOLD_PASS_LEFT and merge_safe:
state.mode = FREE_RUN
# ... abort transitions, emergency overrides ...
Proposed -- Scenic state-block syntax
behavior TacticalPlanner():
state FREE_RUN:
when (strategy == 'pass_left'):
goto COMMIT_PASS_LEFT
when (strategy == 'pass_right'):
goto COMMIT_PASS_RIGHT
state COMMIT_PASS_LEFT:
on entry:
state.commit.side = 'left'
state.commit.start_s = sim_time
take SetTtl('left')
when (lateral_clear):
goto HOLD_PASS_LEFT
when (path_collision_predicted):
goto ABORT_PASS
state HOLD_PASS_LEFT:
when (merge_safe): goto FREE_RUN
> src/scenic/domains/racing/tactical_planner.py:330-396
Feedback
44 / 46

## Slide 45
Recap: 3 Topics, 2 Asks
• Topic 1: scenario banks (F-bank + falsifiable)
• Topic 2: racing library (RacingCar + MPC behavior + tactical planner + falsifier loop)
• Topic 3: dSPACE bridge (light architectural sketch)
• Asks: First-class Frenet frame; first-class state-machine behaviors
Close
45 / 46

## Slide 46
Thanks For Listening
Open the floor for questions
Close
46 / 46